## Slide 1
4230 Optimized refocusing flip angle train design for small peripheral nerve imaging with 3D TSE
Barbara Cervantes1, Jan S. Bauer2, Hendrik Kooijman3, Marcus Settles1, Axel Haase4, Ernst J. Rummeny1, Klaus Wörtler1, Dimitrios C. Karampinos1
1Department of Diagnostic & Interventional Radiology, Technische Universität München, Munich, Germany
2Department of Neuroradiology, Technische Universität München, Munich, Germany
3Philips Healthcare, Hamburg, Germany
4Zentralinstitut für Medizintechnik, Technische Universität München, Garching, Germany
Computer No: 22

## Slide 2
Declaration of Financial Interests or Relationships
Speaker Name: Barbara Cervantes
I have the following financial interest or relationship to disclose with regard to the subject matter of this presentation:
Company Name: Philips Healthcare
Type of Relationship: Grant Support

## Slide 3: Motivation
1Chhabra, AJR 196:583 2011 2Soldatos, RadioGraphics 33:967 2013
3Yonemaya, Proc. ISMRM p2721 2011 4Busse, Magn Reson Med 60:640 2008
Optimize delineation of small nerves with 3D TSE
High isotropic resolution T2 weighted imaging of peripheral nerves at 3T1
3D imaging of peripheral nerves:
  multi-planar reconstructions
  areas with high obliqueness2
Flip angle modulation in 3D TSE to improve image quality3,4
ax
cor
sag
High-resolution 3D imaging

## Slide 4: 3D TSE imaging of peripheral nerves
Busse, Magn Reson Med 55:1030 2006
1Busse, Magn Reson Med 55:1030 2006 2Busse, Magn Reson Med 60:640 2008
3Weigel, J Magn Reson Imag in press 2014 4Hennig, Magn Reson Med 51:68 2004
Traditional design of flip angle trains
Modulation of flip angles defines shape of MTF
Shape of MTF determines signal intensity and blurring1,2
EPG: compute flip angles from desired MTF1,3,4
MTF
Flip angle train
  Design tissue-specific flip angle trains2
EPG

## Slide 5: 3D TSE imaging of peripheral nerves
1Constable, Magn Reson Med 28:9 1992 2Chen Proc. Intl. Soc. Mag. Reson. Med. 21 p.3716 2013
Geometry considerations in optimization of flip angle trains
Small objects: blurring of surrounding tissue affects signal1
Geometry conditions in optimization of flip angle trains2:
  tissue- and geometry-specific design
Constable, Magn Reson Med 28:9 1992
signal of small embedded objects highly sensitive to shape of MTF
constant

## Slide 6: Purpose
To include geometry considerations into the design of flip angle trains in 3D TSE to generate optimal delineation of small nerves.

## Slide 7: Methods
Design shape of desired MTF
Computation of flip angle trains
MTF
Flip angle train
  signal plateau
Sequence parameters
T1, T2 of reference tissue
  tissue-specific flip angle train
EPG

## Slide 8: Methods
*Carried out for muscle and suppressed fat
Computation of flip angle trains and MTFs in parameter subspace:
  echo spacing: [2.5ms,5ms]
  signal plateau: [0.5*etl,etl]
Simulated signal profiles:
  three nerve geometries
  blurring with MTFs
Signal simulations
infinite nerve
  assess signal and width variations induced by blurring of surrounding tissue*
finite width
1-pixel width
Signal of embedded nerve:
example of simulated signal profile

## Slide 9: Methods
B
C
Introduced metrics:
  deviation from maximum signal:
  joint deviation from maximum signal and minimum width:
Flip angle train optimization
1-pixel nerve
embedded in muscle
embedded in suppressed fat*
S: nerve signal
b: nerve width
  |Smax-S|/Smax
  |Smax-S|/Smax + |bmin-b|/bmin
(i)
(ii)
(i)
(ii)

## Slide 10: Methods
B
C
**3D TSE in peripheral nerve imaging usually performed with fat suppression
Flip angle trains for nerve in muscle:
  B: maximizes nerve signal
  C: optimizes signal and blurring
Flip angle trains for nerve in suppressed fat**:
  B*
  C*
Flip angle train optimization
1-pixel nerve
embedded in muscle
embedded in suppressed fat

## Slide 11: Methods
*Main focus: small nerves embedded in muscle
Lumbar plexus of 10 healthy volunteers on 3 T Philips Ingenia scanner
T2-weighted 3D TSE with*:
  flip angle train B
  flip angle train C
Echo spacing=4ms, max. flip angles=[100°125°], 6 initial echoes, FOV=400×400×80mm3, acq. voxel=1.25×1.25×1.4 mm3, reconstruction voxel=0.63×0.63×0.7 mm3, TR/TE=2000/330ms, TSE factor=150, scan duration=4min26s, reference tissue T1=1010ms and T2=90 ms, parallel imaging with reduction factor R=2.5, no partial Fourier, fat suppression with SPAIR, flow suppression with iMSDE with VENC=1cm/s
In vivo measurements
Flip angle trains:
B: maximum signal
C: optimized
Abstract #101: Power Poster on Monday June 1st 14:15

## Slide 12: Methods
*Relative to flip angle train B
Signal profiles along:
  large L5 nerves
  small L3 nerves
Nerve signal normalized to muscle
To compare flip angle trains B and C measured:
  nerve signal SB and SC
  nerve width bB and bC
  signal variation* (SC-SB)/SB
  width variation* (bB-bC)/bB
Data analysis
Flip angle trains:
B: maximum signal
C: optimized

## Slide 13: Results
Comparison of flip angle trains
Flip angle trains:
B: maximum signal
C: optimized
...
small L3 nerves
large L5 nerves
example: single profile
not relevant
not relevant
not relevant
not relevant
Flip angle train B:
Large nerves 25% higher signal than small nerves

## Slide 14: Results
Comparison of flip angle trains
Flip angle trains:
B: maximum signal
C: optimized
...
small L3 nerves
large L5 nerves
example: single profile
not relevant
not relevant
not relevant
not relevant
Flip angle train C:
Large nerves 11% higher signal than small nerves

## Slide 15: Results
Comparison of flip angle trains
Flip angle trains:
B: maximum signal
C: optimized
...
small L3 nerves
large L5 nerves
example: single profile
not relevant
not relevant
not relevant
not relevant
Signal loss with flip angle train C compared to B: mostly large nerves

## Slide 16: Results
Comparison of flip angle trains
Flip angle trains:
B: maximum signal
C: optimized
...
small L3 nerves
large L5 nerves
example: single profile
not relevant
not relevant
not relevant
not relevant
Width improvement with flip angle train C compared to B: significant for small nerves

## Slide 17: Results
Flip angle train C compared to B
Overall reduction of:
  signal
  blurring
Large nerves: more uniform signal (red arrows)
Small nerves: improved delineation (yellow arrows)
Flip angle trains:
B: maximum signal
C: optimized
subject 1
subject 2

## Slide 18: Discussion
In peripheral nerve imaging with 3D TSE:
Tissue-specific flip angle modulation frequently implemented1,2
Blurring greatly affects delineation of small nerves
Coupling of signal of small nerves and blurring of surrounding tissue
Need to consider geometry-specific blurring effects in flip angle modulation
1Kasper, Eur Radiol 2015 2Chhabra, Skeletal Radiol 40:1249 2011
Optimized flip angle train C: best balance of signal and sharpness of small nerves embedded in muscle

## Slide 19: Discussion
Optimized flip angle train C:
Significantly improves delineation of small nerves
Generates signal uniformity across all nerve sizes
Also optimizes delineation of nerves in suppressed fat
Limitations:
Signal loss compared to (standard) B:
  most signal loss in large nerves
  (!) not recommended for scans with low SNR
Optimization in selected parameter space (protocol-dependent)
Limited relaxometry literature in peripheral nerve imaging in humans

## Slide 20: Conclusion
An optimized flip angle train in 3D TSE considering geometry-specific blurring effects of the surrounding tissue significantly improves the delineation of small peripheral nerves.
Dedicated flow suppression preparation in peripheral nerve imaging with 3D TSE:
Abstract #101: Power Poster on Monday June 1st 14:15

## Slide 21
Acknowledgements
Funding: Philips Healthcare